## Slide 1: Ocean Colour Thematic Assembly Center - MED
Gianluca Volpe
Italian National Research Council
Regional User Training Workshop
La Spezia, December 4th, 2015

## Slide 2: Outline
Background info on OCTAC system
Background info on Ocean Colour
OCTAC product info
  Use of Reflectances
  Use of Chl measurements
Navigating the Catalogue

## Slide 3: OCTAC MyOcean heritage
The OCTAC is a distributed system which acts as a Production Centre of high-quality OC products
It provides operational service to Copernicus Marine Environment Monitoring Service (CMEMS) - the legacy of GMES
The OCTAC Ocean regions are: GLO (global ocean), EUR (Pan-European Seas), ARC (Arctic Ocean), BAL (Baltic Sea), ATL (Atlantic Ocean), BS (Black Sea), and MED (Mediterranean Sea).

## Slide 4: CMEMS OC TAC: Architecture evolution

## Slide 5: CMEMS OC TAC: Architecture evolution

## Slide 6: CMEMS OC TAC: Architecture evolution
Regional ad hoc algorithms operationally implemented

## Slide 7: OCTAC Products
Ocean Optics
  Rrs (l)
  Kd
TWO main product categories
Ocean Optics
Ocean Chlorophyll
Ocean Chlorophyll
  Case I (no longer available in V2)
  Merged Case I - Case II
Products (names or codes) may differ with respect to
the Timing of Release (NRT/DT or REP)
Products may include several datasets (Sat. sensors)

## Slide 8: Timing of Product release
NRT with preliminary or no ancillary data
(same or next day)
DT with final ancillary data
(after 5 days)
  Currently under investigation and sensible to change from April 2016
REP when improved Cal/Val affords improved products
(once a year)

## Slide 9: OCTAC Products
Ocean Optics
  Rrs (l)
  Kd
TWO main product categories
Ocean Optics
Ocean Chlorophyll
Ocean Chlorophyll
  Case I (no longer available in V2)
  Merged Case I - Case II
Products (names or codes) may differ with respect to
the Timing of Release (NRT/DT or REP)
Processing Level (L3 or L4)
Products may include several datasets (Sat. sensors)

## Slide 10: Processing Levels
L2: this is the input data from space agency
L3: geophysical product (1 km)
  daily resolution
  all swaths over the spatial domain combined together
L4: geophysical product
  averaged over weekly and monthly time scale (1 km)
  interpolated (data voids due to clouds filled by statistical methods) (4 km)
    1 km, from April 2016 (CMEMS V2)

## Slide 11: OC Basic Info
LIGHT emitted from the sun INTERACTS with the SEAWATER and its CONSTITUENTS before being captured by the remote sensor
Ocean Colour is the description of the optical properties of the medium through which the light propagates

## Slide 12: OC Basic Info
The bulk, or large-scale, optical properties of water are conveniently divided into two mutually exclusive classes: INHERENT and APPARENT.
LIGHT emitted from the sun INTERACTS with the SEAWATER and its CONSTITUENTS before being captured by the remote sensor

## Slide 13: OC Basic Info
The bulk, or large-scale, optical properties of water are conveniently divided into two mutually exclusive classes: INHERENT and APPARENT
INHERENT OPTICAL PROPERTIES (IOPs) are those properties that depend only upon the medium, and therefore are independent of the ambient light field within the medium
Light emitted from the sun INTERACTS with the SEAWATER and its CONSTITUENTS before being captured by the remote sensor

## Slide 14: OC Basic Info
The bulk, or large-scale, optical properties of water are conveniently divided into two mutually exclusive classes: INHERENT and APPARENT
APPARENT OPTICAL PROPERTIES (AOPs) are those properties that depend both on the medium (the IOPs) and on the geometric (directional) structure of the ambient light field, and that display enough regular features and stability to be useful descriptors of the water body
Light emitted from the sun INTERACTS with the SEAWATER and its CONSTITUENTS before being captured by the remote sensor

## Slide 15: OC Basic Info
Ed(l,z)
The spectral downwelling Irradiance (Ed) is the total amount of light reaching a surface area element, from all the upward directions

## Slide 16: OC Basic Info
Ed(z) Ed(0-)e-Kdz
Ed(l,z)
April 12th, 2014
The spectral downwelling Irradiance (Ed) is the total amount of light reaching a surface area element, from all the upward directions

## Slide 17: OC Basic Info
Kd
Ed(z) Ed(0-)e-Kdz
is the vertical attenuation coefficient for downward irradiance and describes the rate of change of Ed(l) with depth

## Slide 18: OC Basic Info
Kd
Ed(z) Ed(0-)e-Kdz
is the vertical attenuation coefficient for downward irradiance and describes the rate of change of Ed(l) with depth
has units of m-1
smaller Kd values
less attenuation
greater water Transparency

## Slide 19: OC Basic Info
Kd = 0.01 m-1
Ed(1m) = 90% Ed(0-)
Ed(1m) = 36% Ed(0-)
Ed(z) Ed(0-)e-Kdz
Ed(1m) = 99% Ed(0-)
Kd = 0.1 m-1
Kd = 1 m-1

## Slide 20: OC Basic Info
Ed(z) Ed(0-)e-Kdz
Ed(l,z)
April 12th, 2014
Zeu ~ 1% PAR (0+)
Zpd ~
Zeu
4.6

## Slide 21: OC Basic Info
Lu(l,z)
The spectral upwelling Radiance (Lu) is the amount of light reaching a surface area element, through one solid angle

## Slide 22: OC Basic Info
Zeu
Zpd
April 12th, 2014
Lu(l,z)
The spectral upwelling Radiance (Lu) is the amount of light reaching a surface area element, through one solid angle

## Slide 23: OC Basic Info
Zeu
Zpd
April 12th, 2014
Lu(l,z)

## Slide 24: OC Basic Info
Lu
Rrs(l,0+) ~
Ed

## Slide 25: OC Basic Info
Lu
Rrs(l,0+) ~
Ed

## Slide 26: OC Basic Info
Lu
Rrs(l,0+) ~
Ed
The quantity of interest to us

## Slide 27: OC Basic Info
Lu
Rrs(l,0+) ~
Ed
MBR =
MAX(RrsBlue)
RrsGreen
< 550 nm
~ 550 nm
Maximum Band Ratio

## Slide 28: OC Basic Info
Open ocean
Optical signal variability is WELL explained by the variability in phytoplankton biomass
(i.e., Chlorophyll)
Case I waters
Coastal waters
Optical signal variability is ONLY PARTIALLY explained by the variability in phytoplankton biomass
CDOM & TSM can play a significant role
Case II waters

## Slide 29: Chlorophyll
April 12th, 2014

## Slide 30: Chlorophyll
Zeu
April 12th, 2014

## Slide 31: Chlorophyll
Zpd
Zeu
April 12th, 2014

## Slide 32: Chlorophyll
Zpd
Zeu
April 12th, 2014

## Slide 33: Chlorophyll
Zpd
Zeu
April 12th, 2014
Important: OC gives you information about the surface ocean!

## Slide 34: MedOC in situ dataset
Bio-optical measurements
> 800 Chl/Opt measurements to define the Mediterranean regional algorithms for Case I waters

## Slide 35: MedOC in situ dataset
Bio-optical measurements
> 800 Chl/Opt measurements to define the Mediterranean regional algorithms for Case I waters
Chl Profiles
> 2600 chlorophyll profiles for satellite data VALIDATION

## Slide 36
UNIQUE in situ dataset to develop sensor-specific algorithms for Case I waters
MERIS
SeaWiFS
MODIS
VIIRS

## Slide 37
UNIQUE in situ dataset to develop sensor-specific algorithms for Case I waters
MERIS
SeaWiFS
MODIS
VIIRS
Chl < 0.5 mg m-3
Global algorithms systematically overestimate in situ measurements
Statistically, 0.5 mg m-3 comprises more than 75% of the data values (not only in situ)

## Slide 38
UNIQUE in situ dataset to develop sensor-specific algorithms for Case I waters
MERIS
SeaWiFS
MODIS
VIIRS
Chl > 0.5 mg m-3
Global and Regional overlap

## Slide 39
Case II water Algorithm
Case II water Algorithm: AD4
D’Alimonte & Zibordi [2003]
Case II
ChlCase II < ChlCase I
Chl = 0.4 mg m-3
ChlCase II > ChlCase I
Case I
MBR = 1.9

## Slide 40
Case I - Case II Chl MERGING
ChlMerged
ChlCaseID2CaseI + ChlCaseIID2CaseII
D2CaseI + D2CaseII
=
On a pixel-by-pixel basis, the satellite Rrs spectrum is compared with the distributions of the two in situ datasets: Case I and Case II
The Mahalanobis distance parameter is used for quantifying the distance of the ith satellite pixel spectrum, x, from the reference in situ datasets, µ

## Slide 41
Case I water Algorithm
Blue
Green
Chl Case I
MBR
Rrs443
Rrs488
Rrs547

## Slide 42
Merging Case I – Case II
Blue
Green
MBR
Rrs443
Rrs488
Rrs547
MERGED Chl

## Slide 43
Merging Case I – Case II
Chl Case I

## Slide 44
Merging Case I – Case II
Merged Chl

## Slide 45
Level 3 & Level 4 Products
To fill in initial gaps and to initialize the EOF procedure, Daily Observations and Daily Climatology are combined via Smoothing Procedure method
Level 3

## Slide 46
To fill in initial gaps and to initialize the EOF procedure, Daily Observations and Daily Climatology are combined via Smoothing Procedure method
Level 3 & Level 4 Products
Input

## Slide 47
Level 4
To fill in initial gaps and to initialize the EOF procedure, Daily Observations and Daily Climatology are combined via Smoothing Procedure method
Level 3 & Level 4 Products

## Slide 52
REP products derived
from ESA-CCI
New version available (April, 2016) with data up to 2014

## Slide 53
Quality Index
QI =
CurrentDataPixel - ClimatologyDataPixel
STDDataPixel

## Slide 54
Quality Index
QI =
CurrentDataPixel - ClimatologyDataPixel
STDDataPixel

## Slide 55
Quality Index
QI =
CurrentDataPixel - ClimatologyDataPixel
STDDataPixel

## Slide 56
Quality Index

## Slide 57: http://marine.copernicus.eu

## Slide 58
Case I & Case II Chl data merging
Case I
Case II
NOVEL
0.03
10.0
3.2
1.0
0.32
0.10
1
2
3

## Slide 59: Panoply MAP config
Center Lon: 15.25
Center Lat: 38
Width: 42.5
Height:16

## Slide 60: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 61: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 62: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 63: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 64: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 65: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 66: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 67: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 68: Navigating Med Sea Products in CMEMS Online Catalog

## Slide 69: Navigating Med Sea Products in CMEMS Online Catalog